## Slide 1: Indirect Rebound Involving Embodied Energy Use in Re-spending Decisions
How Do We Treat Negative Multiplier Effects in Energy Supply Chains?
IAEE Conference, Bergen 21 June 2016
Project Title: ‘Energy Saving Innovations and Economy-Wide Rebound Effects’
Project web-site: http://www.cied.ac.uk/research/impacts/energysavinginnovations
EPSRC Grant Ref. EP/M00760X/1
Karen Turner and Antonios Katris
Centre for Energy Policy
University of Strathclyde

## Slide 2: What is rebound effect?
Increased energy efficiency leads to monetary savings of households
  Incentive to consume more energy (direct rebound)
  More consumption of non-energy goods (indirect rebound)
  Full economic adjustment (economy-wide rebound)
Rebound effect is the difference between the anticipated and the actual energy savings

## Slide 3: How do we study rebound effects?
Rebound indicator is used to study rebound effects
  The formula used is:
  Ratio of Actual Energy Savings (AES) over Potential Energy Savings (PES)
If R positive then actual savings smaller than potential savings
  As long as R<100% we have net energy savings
  R>100% shows backfire, larger energy use than energy savings
R can be negative – More savings that expected
  Superconservation and/or Turner (2009) negative multiplier effects in energy supply chain

## Slide 4: Is rebound indicator effective?
R indicates our failure to correctly estimate/realise the savings from improved energy efficiency
There is no standard definition of what is included in PES
Guerra and Sancho (2010) and Turner (2013) present completely different approaches

## Slide 5: What is our goal?
We want to highlight the different results under different interpretations of PES
  Turner (2013) – PES = engineering savings
  Guerra and Sancho (2010) – PES = engineering savings + quantity adjustment
  They both agree on using IO to calculate quantity adjustment
Can we get the same information using a different indicator?
Transparency on the economy-wide impacts of improved energy efficiency is key
  Methodology disaggregates supply chains in IRIO
  Use of WIOD data for 2009

## Slide 6: An illustrative example
We assume a 10% reduction in UK household ‘Electricity, Gas and Water Supply’ spending ($5,525m) due to improved energy efficiency
 |  | Energy use (terajoules) | Related CO2 (kilotonnes) | 
 | A. Reduction in direct energy use by UK households | -152,591 | -6,172 | 
 | Reductions in energy use in UK EGWS supply chains: |  |  | 
 | Total multiplier effect per $1m spend: | 38.14 | 1.89 | 
 | B. Direct - own-sector (25.9tj/1.26kt per $1m) | -143,142 | -7,777 | 
 | C. Indirect - own-sector (8.33tj/0.41kt per $1m) | -46,040 | -2,501 | 
 | D. Indirect - other UK (1.06tj/0.08kt per $1m) | -5,878 | -471 | 
 | Sub total UK | -195,060 | -10,749 | 
 | E. Indirect - outside of UK (2.84tj/0.15kt per $1m) | -15,713 | -926 | 
 | Global total | -210,773 | -11,675 | 
 | Total reduction in UK energy use | -347,651 | -16,921 | 
 | Total reduction in global energy use | -363,364 | -17,847 | 
 | Ratio of Total global reduction over direct reduction | 2.38 | 2.89 | 

## Slide 7: Rebound effects in our example
 | Energy use | CO2
Actual energy savings (AES): |  | 
UK level | 347,651 | 16,921
Global level | 363,364 | 17,847
Potential energy savings and rebound: |  | 
Guerra and Sancho (2010) - all included in PES |  | 
UK level: |  | 
PES (A, B, C, D) | 347,651 | 16,921
Rebound | 0% | 0%
Global level |  | 
PES (A, B, C, D, E) | 363,364 | 17,847
Rebound | 0% | 0%
Turner (2013) - only household direct saving included in PES |  | 
UK level: |  | 
PES (A) | 152,591 | 6,172
Rebound | -128% | -174%
Global level: |  | 
PES (A) | 152,591 | 6,172
Rebound | -138% | -189%

## Slide 8: Re-spending the savings
We examine the illustrative scenario that all of the savings are spent on the UK ‘Hotels and Restaurants’ sector
 | Energy use (terajoules) | Related CO2 (kilotonnes)
Increases in energy use in UK Hotels and Restaurants supply chain: |  | 
Total multiplier effect per $1m spend: | 2.84 | 0.14
F. Direct - own-sector (0.41tj/0.02kt per $1m) | 2,287 | 101
G. Indirect - own-sector (0.001tj/0.000kt per $1m) | 6 | 0
H. Indirect - other UK (1.48 tj/0.94kt per $1m) | 8,199 | 413
Sub total UK | 10,492 | 514
I. Indirect - outside of UK (0.94tj/0.05kt per $1m) | 5,218 | 279
Global total | 15,711 | 794
Net increase/decrease in UK and global energy use: |  | 
Change in direct energy use by UK households (A) | -152,591 | -6,172
EGWS shock: change in direct EGWS energy use (B) | -143,142 | -7,777
Change in other UK energy use (C, D, F, G, H) | -41,426 | -2,458
Net at UK level | -337,159 | -16,406
Change in energy use outside of UK (E and I) | -10,495 | -646
Net at global level | -347,654 | -17,053

## Slide 9: Indirect rebound from re-spending
 | Energy use | CO2
Actual energy savings (AES): |  | 
UK level | 337,159 | 16,406
Global level | 347,654 | 17,053
Rebound: |  | 
Guerra and Sancho (2010) - all included in PES |  | 
UK level: | 3% | 3%
Global level: | 4% | 4%
Turner (2013) - only household direct saving included in PES |  | 
UK level: | -121% | -166%
Global level: | -128% | -176%

## Slide 10: The saving multiplier
Instead of R as an indicator we propose the use of an energy use/carbon saving multiplier (CSM)
Multipliers are commonly used to inform policies - policy makers are familiar with multiplier analysis
CSM can be also be used in other contexts like waste generation

## Slide 12: What is the meaning of CSM?
CSM reports the additional emissions savings achieved, per unit of emissions saved at the household level
Mostly positive but eroded by re-spending of savings
Policy focus to limit the erosion of the CSM

## Slide 13: Thank you for your attention
For any questions and/or suggestions please feel free to contact us
karen.turner@strath.ac.uk
antonios.katris@strath.ac.uk
The paper from which the results were drawn is available at the conference online proceedings:
http://www.iaee.org/iaee2016/submissions/OnlineProceedings/IAEE%2039_2016TurnerKatris_on-line%20proceedings.pdf
Also available as a working paper at:
http://strathprints.strath.ac.uk/55426/
A policy briefing drawn from this paper can be found here:
http://cied.ac.uk/files/file.php?name=multiplier-analysis-of-re-spending-rebound-effects.pdf&site=440
EPSRC project website:
http://www.cied.ac.uk/research/impacts/energysavinginnovations